## Slide 1: Embedded Systems Introduction

## Slide 2: Reminders
Class Mon/Wed/Fri
  Mon / Wed in person WAL A420 9 – 9:50am
  Friday is ONLINE 9 – 9:50am
    These will be working group sessions
    If you have completed the demo or lab for that given day ahead of time attendance is not required.
  Obtain DE1-SoC board
    Follow instructions in announcements
  Download Quartus Prime Lite 18.1
    Be sure it is 18.1 or you will have a tool variation from the labs
Review Syllabus and Schedule
  myCourses overview

## Slide 3: Schedule This Semester
Complete first Quiz – Due Sunday
  Quizzes section of myCourses
  Each week quizzes will cover material from lecture
  Typically 10 questions, 15 minutes
    Be sure to review weeks material before you take the quiz!
Complete first Demo assignment – Due Friday
  Dropbox video or documentation on myCourses
Lab due dates posted in schedule
  No reports
  Zip entire project for reproduction
  Paper signoffs
  TA: Santi Sanchez

## Slide 4: What is an Embedded System?
Any system that includes a programmable computer, but is not itself a general purpose computer
A microprocessor-based system that is built to control a function or a range of functions and is not designed to be programmed by the end user
A system designed to perform one specific task and is optimized for that application

## Slide 5: Problems With Given Definition
Field is outgrowing traditional descriptions as technology advances and cost of implementation of various hardware and software components decreases.
Devices such as smart phones designed to do a variety of functions and run a variety of applications.
Where does the iPad fit in?

## Slide 6: How Do Embedded Systems Differ From PCs?
Embedded System
Specific application that is known at design time
Not programmable by end user
Optimized for fixed run-time requirements
Criteria
  Cost
  Reliability
  Power consumption
  size
PC
Broad class of applications
Programmable by end user
Faster is better
Criteria
  Cost
  Average speed

## Slide 7: Components of an Embedded System
Data Memory
(Volatile)
Program Memory
(Non-volatile)
Micro-processor
Input/Output
Processor
Memory
I/O

## Slide 8: Components of an Embedded System (iPhone 4)
top
view
bottom
view
256G x8
Flash
Touch
Screen
Controller
128 M-Bit SDRAM
ARM Processor
I/O
ROM
RAM
CPU

## Slide 9: Characteristics of Embedded Systems
Must be dependable:
  Higher quality and reliability requirements than other types of computer systems
  Control critical functions
    medical applications
    automobile safety features
    security measures
    military applications
    and more ….

## Slide 10: Characteristics of Embedded Systems
Must be efficient:
  Consumers are demanding
  Mass-market items must have low manufacturing costs
  So… systems need to be
    Energy efficient – many are battery powered
    Code-size efficient – memory size is limited to keep device small
    Weight efficient
    Cost efficient

## Slide 11: Characteristics of Embedded Systems
Must meet real-time constraints:
  A real-time system must react to stimuli immediately
  Must finish operations by deadlines
    Hard constraint: missing deadline causes failure
    Soft constraint: missing deadline results in degraded performance

## Slide 12: Characteristics of Embedded Systems
Must meet time-to-market constraints
  Typically 6 to 8 months
Time
Possible Revenue
Market Window

## Slide 13: Embedded System Technologies
Current Technologies
  Microprocessor based
    Available in 8-bit, 16-bit, or 32-bit
    Ex: Intel 80x86, Pentium, PowerPC, ARM
  Microcontroller based
    Specialized processor that include on-chip memory, D2A, A2D, etc
    Ex: TI MSP430, Renesas RX, Freescale, Coldfire, Arduino, etc
  DSP Based
    Processor optimized for mathematical operations
    Ex: Texas Instruments C64x, Analog Device Blackfin
  FPGA Based
Technology moving towards higher level integration
  Discrete components  more functionality per each device
  ASIC / ASSP / SOC / SOPC

## Slide 14: Embedded System Technologies
Application-Specific Integrated Circuit (ASIC)
  Device created with a specific purpose
  Typically designed and used by single company
  Development expensive, time-consuming, & resource-intensive
  High performance coupled with low power consumption
  Algorithm or design fixed in silicon

## Slide 15: Embedded System Technologies
Application-Specific Standard Parts (ASSP)
  Designed and implementation same as ASIC
  More general-purpose device for use by multiple systems
  Marketed to multiple customers with specific application
    Ex: USB interface chip
  High performance coupled with low power consumption
  Algorithm or design fixed in silicon
System-on-Chip (SOC)
  ASIC or ASSP that contains one or more processors
  SOC also contains other stuff
    On-chip memory, hardware accelerator, peripheral, etc
  Algorithm or design fixed in silicon

## Slide 16: Embedded System Technologies
Simplified Relationship Diagram
www.programmableplant.com: ASICs vs. ASSPs vs. SoCs vs. FPGAs

## Slide 17: Embedded System Technologies
Field Programmable Gate Array (FPGA)
  Programmable logic device that is configured by designer
    “Sea of Gates”
    Require programming before using (SRAM based)
  Development is inexpensive and easier to perform
    Shorter cycles between development & prototyping
    Easy to change, modify or expand design
  High power consumption with lower performance
System-on-Programmable-Chip (SOPC)
  Basically same as an SOC but in programmable device
    A very large FPGA that takes the place of ASIC/ASSP
  Development is inexpensive and easier to perform
    Allows ASIC / ASSP designer a platform to develop on

## Slide 18: Embedded System Technologies
SOPC (con’t)
  FPGA contains one or more processors
  SOPC also contains on-chip memory, hardware accelerator, peripheral, etc
  Processors, memories, and other components can be built into the FPGA (hard-core) or created from the programmable fabric (soft-core).
  The focus of CPET-561

## Slide 19: Embedded System Technologies
SOPC compared to ASIC or ASSP
  pros
    Short lead times
    Lower NRE (non-reoccurring engineering)
    Design changes are easy (reprogram)
  cons
    Higher power
    Cost is constant despite volume
    Have to choose from off-the shelf parts
      Not optimized

## Slide 20: System on Programmable Chip
Designing an SOPC
Select a chip with required hard-cores (IP)
Add required soft-cores (IP)
Add user logic to tie everything together

## Slide 21: Embedded System Design Considerations
System Partitioning
  Determine where each function should be implemented
    What task is done in hardware?
    What task is done in software?
  Hardest part of embedded design
    How will system be used?
    How should system respond?
    Need to understand who has access to what and when?
  Utilizes Use Cases to define partitioning
    Technique for capturing functional requirements of systems
    Forces you to think how the design partitions interact
    Unified Development Process (UDP)
      Grady Booch and James Rumbaugh
Notes: What is a Software Architecture?
IEEE 1471
  Architecture is the fundamental organization of a system embodied in its components, their relationship to each other, and to the environment, and the principles guiding its design and evolution.
High Level Structure
  No implementation details!
  Language agnostic
The core pieces of a software architecture
  Identifying system components
  Understand how components interact with
    Other components
    Their environment
  Organizing the components into a system that is
    Understandable
    Modular
    Maintainable

## Slide 22: Embedded System Design Considerations
Design Challenges of Embedded System
  How much hardware do we need?
    How big of a processor do we need?
    How much memory do we need?
  How do we meet our design goal?
    Do you use faster hardware or better software optimization?
  How do we minimize power?
    Do you slow system down?
    Do you enable low power modes by shutting sections off?
  How do we test/debug our system?
    How to test real-time aspect?
    What is the design environment?
Notes: Why use a software architecture?
  Define the elements in the design
  Understand relationship of the components
  Describe the structure and behavior of the system
  Identify engineering decisions
  Review and hash out the design before implementation
  Identify holes in the requirements and implementation
How does one create a software architecture?
  Component Lists – just a simple list of components needed (timer, PWM, ADC, PIO, etc)
  Component Layer Architecture – Group components into Application vs driver
  Flow Charts
  Sequence Diagrams – shows interaction between objects (messages or data transfers)
  State Machines
  State Charts – Define state of object during entire life; event driven

## Slide 23: Embedded System Design Flow
How Do You Design (Be honest…)
  Big Bang Model
    No clear requirements or understanding of problem
    No planning or processes in place before or during development
    The reason many students struggle with CPET561 labs
  Code & Fix
    Have some product requirements and understanding in place
    No formal process in place to guide development
  Waterfall
    Have product requirements and understanding in place
    A formal process is defined and development proceeds in steps
  Spiral
    A formal process is defined and development proceeds in steps
    Feedback is obtained and incorporated back into design steps

## Slide 24: Embedded System Design Flow

## Slide 25: Embedded System Design Flow
Product Concept:
Think of this as the lab handout that outlines the concept of the lab. It outlines the basic problem and requirements.

## Slide 26: Embedded System Design Flow
Analysis:
You as the “designer” must analyze the product concept and identify all requirements. Not all requirements will be obvious or be clearly stated. You must ask questions.

## Slide 27: Embedded System Design Flow
Architecture:
Sketch out an architecture that implements requirements. Identify all the major components and define interaction between the components. Let sit for a day or so and return with fresh look.
Notes: Define Requirements
  Hard Real-Time Constraints
  Soft Real-Time Constraints
  Sensors and hardware interfaces
  System Timing
  Human interactions
  Identify synchronous events
  Identify asynchronous events

## Slide 28: Embedded System Design Flow
Review:
Create and apply various use cases to the architecture to determine how the architecture behaves. Ask others for feedback.

## Slide 29: Embedded System Design Flow
Accepted?:
If architecture fails to satisfy all the requirements or meet the customer expectations then find out why and modify the design.

## Slide 30: Embedded System Design Flow
Detail Design: If the architecture satisfies all the requirements and meets the customer’s expectations then start the detailed design work.
Notes: Phase 1 is the most critical for the success of the embedded design. A lot of the time should be allocated here to make your get the design correct.
Phase 1 Can be partitioned into 6 Steps:
  Step 1: Product Concept is created. This is represented by the lab handout the outlines the concept of the lab.
  Step 2:.
  Step 3: Sketch out an architecture that implements design. Identify all the major components define interaction between components.
  Step 4: Review the architecture. Apply various use cases to the architecture and ask others for feedback.
  Step 5: Ask yourself does the design satisfies all the requirements and met customer expectations!
  Step 6: If architecture fails to satisfy all the requirements or met customer expectations then find out why and modify the design.
  Stage 4: If architecture satisfy all the requirements and met customer expectations then start designing.
  Stage 5: Documenting the architecture
  Stage 6: Analyzing and reviewing architecture

## Slide 31: Embedded System Design Flow
Test & Verification:
Test and verify that the design satisfies all requirements. Verify design under all conditions and corner cases.

## Slide 32: Embedded System Design Flow
Accepted?:
If architecture fails to satisfy all the requirements or fails to perform properly then find out why and modify the design.

## Slide 33: Embedded System Design Flow
Sign-off for approval:
If design operates properly and satisfies all the requirements then deliver to customer for final review and approval.

## Slide 34: Embedded System Design Flow
Test & Verification
  Test & Verification are critical to successful design. We don’t just make you do it for our entertainment 
  Sooner bugs or problems are detected, the easier and less expensive they are to fix
    Critical to understand requirements and expectation up front
    Don’t assume you understand the problem or requirements

## Slide 35: Embedded System Design Principles
General Design Principals
  Keep things simple
    Simpler designs are easier to design/code and test
    Designs that have predictable characteristics tend to be simpler
      Avoid special cases
      Ex: Hardware for variable # of operands more complicated than fixed number of operands
  Smaller designs are usually faster
    Larger designs increase propagation delay which reduces Fmax
      Ex: Increasing the number of registers causes the decoder to get larger (increase decode time)
  Make the common case fast
    Concentrate optimization effort on sections that are used often
  Good designs have good compromises
    You can’t have everything, weigh trade-offs carefully