## Slide 1: SOPC and Cores
Week 1 – Lecture 2

## Slide 2: Reminders
Obtain DE1-SoC board from Ken Garland
Download Quartus Prime Lite 18.1
Review Syllabus and Schedule
Complete first Quiz – Due Sunday
  Quizzes section of myCourses
  On material from this weeks lectures
Complete first Demo assignment – Due Friday

## Slide 3: Reminders
FRIDAY CLASSES ARE ONLINE
  We will be reviewing the EDE and any questions about the demo due this week.
No class Monday 9/2 for holiday

## Slide 4: Digital Systems- A Brief History
~1960 discrete transistors (and other solid state devices) became reliable and vacuum tubes were replaced
  First systems consisted of solid state devices on a substrate interconnected with discrete wires

## Slide 5: Digital Systems- A Brief History
~1965 introduction of the integrated circuit
  Systems still consisted of interconnected discrete components
    Not much functionality for the size
    High potential for error in building
    Could not be tested until built

## Slide 6: Digital Systems- A Brief History
1971 – First microprocessor
  Complete system still needed ROM, RAM, timers, etc
  Built from discrete components

## Slide 7: Digital Systems- A Brief History
1974 – First Microcontroller
  Also known as system-on-a-chip
  Has CPU, ROM, RAM, etc. all on same chip
    5,000 transistors
    3000 bits of program memory
    128 bits of access memory

## Slide 8: Digital Systems- A Brief History
1974 – 2018
  Integrated Circuit technology advanced at a breathtaking pace
  System on a Chip (SOC) increase in complexity
    Advanced technology allows for large systems to be placed on a single full-custom integrated circuit
    Negatives
      High NRE (up front costs)
      Long lead times
      Design cannot be modified
    Positives
      Optimized for size
      Low power
      Reduced cost for high volume

## Slide 9: Moore’s Law
Since the invention of the integrated circuit in 1958, the number of transistors that can be placed inexpensively on an integrated circuit has increased exponentially, doubling approximately every two years.
  Think about it……
  ….mind blown

## Slide 10: Moore’s Law

## Slide 11: Where are we now?
1985 first Field Programmable Gate Array (FPGA) was developed
System on Programmable Chip (SOPC) was born
SOPC Compared to custom IC
    Short lead times ( )
    Lower NRE ( )
    Design changes are easy (reprogram) ( )
    Higher power ( )
    Cost is constant despite volume ( for small volumes, for large volumes)
    Have to choose from off-the shelf parts ( )
      Not optimized

## Slide 12: Tradeoffs
Speed,
Density,
Complexity,
Market
Volume
Needed
For
Product
        Engineering Cost, Time to Develop Product
Full custom
VLSI design
ASICs
FPGAs
PLDs

## Slide 13: System on Programmable Chip
Typically includes
  IP (intellectual property) processor core
  Custom hardware
    Timers
    Serial communication interfaces: UART, SPI
    General purpose I/O
    Digital signal processing (DSP) functions
    Communications peripherals
    Interfaces to off-chip devices
      Memory controllers
      Buses and bridges
  Application-specific hardware components
    Developed by the user

## Slide 14: IP Cores in SOPC

## Slide 15: IP Cores
What is Intellectual property (IP)
  Intellectual property refers to creations of the mind
    Inventions, literary and artistic works, and symbols, names, images, and designs
What are IP Cores?
  Ready made function that you can instantiate into your design
  Cores classified as either hard or soft
    Hard Cores
      Design is dedicate circuitry designed in silicon
    Soft Cores
      Designed using LE and general FPGA logic
      Does not physically exist in silicon

## Slide 16: IP Core
What are IP Cores?
  Cores can range in complexity
    Simple arithmetic operators
      Ex: adders, accumulators, and multipliers
    System-level building blocks
      Ex: filters, transforms, and memories
    Specialized functions
      Ex: bus interfaces, controllers, and microprocessors
What are some advantages and disadvantages to using IP cores?

## Slide 17: IP Cores
Benefits of using a Core
  Increase design performance
    Highly optimized for given architecture
  Saves time designing and debugging
    Cores are created by expert designers
    Improves time to market
    Guaranteed functionality
  Spend time on your design where you add value
    Less time spent on commodity design sections
Disadvantages of using an IP Core
  Locks design into an FPGA architecture
    Limits your migration potential to other devices
      Ex: Altera  Xilinx ….. Intel OR AMD?

## Slide 18: Processor Cores
What is a Soft Processor?
  A microprocessor fully described in software, usually in an HDL, which can be synthesized in programmable hardware, such as FPGAs
  Can implement many parallel processors on one FPGA
  Allow designer to define memory, ALU and peripheral functionality
    Resources not used to implement processor can be used for other functionality
What is a Hard Processor
  Processor implemented in silicon
    Processor is actually designed into the FPGA
      Hybrid approach between ASIC and FPGA
    Hard Processor cores are less flexible but have higher performance
Notes: Similar to how a VHDL circuit can be put on a FPGA to allow for high configurability, a soft processor is a processor implemented on a FPGA. This is different than a hard processor, which is a processor implemented in hardware. Soft processor is a logical schematic (software) that can be loaded onto any FPGA. So a soft processor isn’t really a processor, but just a schematic (or code like software). This gives it all the advantages of software such as giving updates and improving the development cycle.

## Slide 19: Processor Cores
What is a Soft Processor?
  A microprocessor fully described in software, usually in an HDL, which can be synthesized in programmable hardware, such as FPGAs
  Highly configurable and customizable to the application
  Can implement many parallel processors on one FPGA
  Allow designer to define memory, ALU and peripheral functionality
  Implemented in the FPGA’s “sea of gates”
    Resources not used to implement processor can be used for other functionality
  Slower clock rates and more power consumption
  Examples: Altera NIOS II, Xilinx Microblaze
Notes: Similar to how a VHDL circuit can be put on a FPGA to allow for high configurability, a soft processor is a processor implemented on a FPGA. This is different than a hard processor, which is a processor implemented in hardware. Soft processor is a logical schematic (software) that can be loaded onto any FPGA. So a soft processor isn’t really a processor, but just a schematic (or code like software). This gives it all the advantages of software such as giving updates and improving the development cycle.

## Slide 20: Processor Cores
What is a Hard Processor?
  The processor is embedded in the silicon of the FPGA
  Does not use the FPGA’s normal logic elements (sea of gates)
    If the hard processor is not implemented in the particular system, its gates are not available for any other use
  Not very configurable
  Higher performance
    Can run at higher clock speeds than Soft-core processor because it is optimize
  Examples: Altera ARM, XILINX PowerPC

## Slide 21: Processor Cores
Altera Cyclone V FPGA
Dedicated hard
core processor
Soft core processor
Built from general
logic

## Slide 22: Processor Cores
Soft Processor vs. Hard Processor
 | Soft Processor | Hard Processor
Configurability | High | Low
Predictability | Low | High
Software Tools | Fewer | More
Speed | Low | High

## Slide 23: Processor Cores
Why use a Soft Processor? (because we will!)
  Higher level of design reuse
  Reduced obsolescence risk
    Design can be modified to accommodate changing requirements
    Easy to add new features and functionality to design
  Increased design implementation options
    Add only processor features that are required by design
    Able to start design w/o all requirements finalized
  Lower latency between processor and FPGA components
    No routing delays to route external processor signal into FPGA
  Can use FPGA logic for accelerating software functions
    Software functions migrated to hardware
    Create custom instructions to access custom hardware

## Slide 24: Using IP Cores
Altera Platform Designer System Builder
Library of Cores from which to choose

## Slide 25: Using IP Cores
Processor
Memory
I/O

## Slide 26: Using IP Cores
Build system in Platform Designer
  Use library of cores
  Interconnect cores with each other, clocks, resets, interrupts, etc.
The tool generates the hardware description language for the system (includes processor design, if using soft core)
The designer instantiates the generated system as a component in the top-level HDL
In the top-level HDL the system component can be integrated with other components developed by the designer