## Slide 1: Altera (Intel) Embedded Design Environment
Week 1 Lecture 3

## Slide 2: HW and SW design
Embedded System Design Flow
  Hardware design flow
    Ex: VHDL, Verilog, etc
  Software design flow
    Ex: C, Assembly
Altera Design Environment
  Supports both hardware and software flow
  Hardware implementation done by Quartus II
  Software implementation done by Nios II Embedded Design Suite (EDS)

## Slide 3: HW and SW Design

## Slide 4: QSYS/Platform Designer(PD) System Builder
System Contents
Main PD Tabs
Component Library
Messages

## Slide 5: Platform Designer
Platform Designer System Builder
  System ID Peripheral
    Used to ensure hardware/software version are synchronized
    Simple 2 registers
      Timestamp
      Random number
    Debugger checks when downloading software to hardware
      Most common connection problem
      Hardware needs to be recompiled and downloaded
    Can be read at runtime to make sure correct hardware is present

## Slide 6: Platform Designer
PD System Builder
  Generates synthesizable output files of the hardware system
    Includes the NIOS II processor and IP cores
    Compiled with the Quartus II software
  Generates “PD Interconnect” to connect components together
    Avalon-MM (Memory Mapped) interfaces
      E.g. Nios II instruction and data masters
    Avalon-ST (Streaming) interface
  XML file used by software tools
    Describes hardware for software build process

## Slide 7: SW Environment

## Slide 8: Software Build Tools
Projects
Terminal Window
File Viewer
Outline View
(View functions, enums, classes, structs etc.)
Select Perspective
Note: NIOS II

## Slide 9: Software Build Tools
Application project
(Contains application source code)
BSP project
(Contains system header file and links to device driver source code)
Note: NIOS II

## Slide 10: Software Build Tools
Perspective Selector
View/modify
(Variables, registers, memory…)
Double-click to add breakpoints
Run project
Debug project
Note: Debug

## Slide 11: Debug Perspective
Resume
Suspend
Terminate
Step Into
Step Over
Step Return

## Slide 12: Generated Files
Important Files
  Quartus Project File (*.QPF)
    Text file that contains basic information about the current version of the Quartus II software and the date
    It also lists all of the revisions created for the project
  Quartus Settings File (*.QSF)
    Text File that contains all of the project-wide and entity-level assignments and settings for the current revision of the project.
  Quartus System File (*.QSYS)
    Text file that records system designed in Platform Designer application
    Contains project name, module names, interface connection, parameters for system

## Slide 13: Generated Files
Important Files
  Quartus IP File (*.QIP)
    Text File that contains path to all the files for IP cores
    Allows you to add required files to Quartus project by adding this file to Quartus instead of adding them individually to Quartus
    Regenerated when PD design is generated
    Added automatically to project when PD opened within new project
  Executable and Linkable Format (elf file )
    Located in Application Project Folder
    Executable and linkable format, compiled output code for download
  System description header file: System.h
    Generated with BSP (located in BSP folder)
    Contains memory map of peripherals and symbolic names

## Slide 14: Software Projects
Nios II Software Project Types
  BSP
    Specialized library containing system-specific support code
    Provides software runtime environment customized for processor in Nios II hardware system
    Contains HAL and device drivers
      HAL provide abstraction away from hardware to make software coding easier
  Application Project
    Contains user code
    Also consists of a collection of source code and makefile
    Used to create executable to run on Nios II processor

## Slide 15: Other Tools
SignalTap II Logic Analyzer
  Embedded Logic Analyzer internal to FPGA
  Allows you to capture signal in your design
    Capture at full system speed
  Uses memory resources to store samples
  Can be used with Nios II Eclipse
SignalProbe
  Routes signals under debug out to spare/reserved pins