## Slide 1: Assembly Language in NIOS II

## Slide 2: Reminders
Assembly demo due Friday
No quiz this week
No lab due this week
  Get your boards if you haven't already done so
Lab 1 due next week at the beginning of your lab session
  See lab for late penalties
  Signoffs can be received in first 15 minutes of lab session or during office hours

## Slide 3: What is Assembly Language?
Low-level programming language for a computer
One-to-one correspondence with the machine instructions
Specific to a given processor
Uses:
  Mnemonics to represent the names of low-level machine instructions
  Labels to represent the names of variables or memory addresses
  Directives to define data and constants
  Macros to facilitate the inline expansion of text into other code

## Slide 4: Directives
Provide information to the assembler
  Do not correspond with an assembly language instruction or data
  Always begin with .
Commonly used directives
  .ascii “string”
    A string of ASCII characters is loaded into consecutive byte addresses in the memory. Multiple strings, separated by commas can be specified
  .asciz “string”
    Same as .ascii, except that each string is terminated by a zero byte
  .data
    Identifies the data that should be placed in the data section of the memory

## Slide 5: Directives
Commonly used directives
  .end
    Marks the end of the source code file
  .equ symbol, expression
    Sets the value of symbol to expression
  .global symbol
    Makes symbol visible outside the assembled object file
  .include “filename”
    Provides a mechanism for including supporting files in a source program
  .space size
    Allocates size bytes to be used for storage

## Slide 6: Directives
Commonly used directives
  .text
    Identifies the code that should be placed in the text section of memory
  .word expression
    Expressions separated by commas are specified. Each expression is assembled into a 32-bit number
    Similar .byte expression available

## Slide 7: Labels
Represents the memory address of the data or instruction marked with that label
  The assembler replaces each label with its memory address when generating the executable
  Must start at the beginning of the line with no leading spaces
  Ex: loop: #read from r2 and store to r3
  ldbio r4, 0(r2)
  stbio r4, 0(r3)
  br loop
  When this code is assembled, the memory address of the ldbio instruction will be inserted in the br instruction

## Slide 8: Registers
NIOS II has 32 internal registers
  Registers hold a 32 bit value
  R0 always holds 0. Writing to R0 has no effect.
  R1 is for the assembler – don’t use in programs
  Registers r24, r25, r27, r28, r29 and r30 all have special uses by the processor
  R31 holds the return address for subroutine

## Slide 9: Registers

## Slide 10: Instruction Types
Approximately 100 instructions
3 types
  R-type : uses 3 registers
    add rC, rA, rB rC <= rA + rB
    sub r2, r16, r15 r2 <= r16 - r15
    mul r3, r5, r6 r3 <= r5 * r6
    div, and, or, nor, xor, etc….
31 27 26 22 21 17 16 6 5 0
A | B | C | OPX | OP

## Slide 11: Instruction Types (Con’t)
  I-type : uses 2 registers and an immediate operand
    Immediate operand is a 16 bit number
    addi rB, rA, IMMED16 rB <= rA + IMMED16
    subi r2, r16, -4 r2 <= r16 – (-4)
    muli r3, r4, 100 r3 <= r4 * 100
    andi, ori, xori, etc…
    No divi
31 27 26 22 21 6 5 0
A | B | IMMED16 | OP

## Slide 12: Instruction Types (con’t)
J-Type
  Does not use registers
  Has a 26 bit immediate operand
  Immediate operand is the address of a subroutine
  Only call instruction
    call IMMED26
    call $0231F0C4
    call Subroutin2
  31 6 5 0
IMMED26 | OP

## Slide 13: Common Instructions
Arithmetic
  add, addi
  sub, subi
  mul, muli
  div, divu (divide unsigned)
Logic
  Bitwise operations
  and, andi
  or, ori
  nor, nori
  xor, xori

## Slide 14: Common Instructions (con’t)
Comparison
  cmpeq rC,rA,rB // rC <= 1 if rA = rB
  cmpne rC,rA,rB // rC <= 1 if rA != rB
  cmplt rC,rA,rB // rC <= 1 if rA < rB
  If comparison is not true, rC <= 0
  Other options for unsigned comparisons
  Immediate comparisons also exist
    cmpeqi rB,rA,IMMED16 //compares rA to constant
    cmpnei rB, rA,IMMED16
    Etc..

## Slide 15: Common Instructions (con’t)
Shifts
  srl rC,rA,rB rC <= rA >> rB
  srli rC,rA,IMMED5 rC <= rA >> IMMED5
  sra rC,rA,rB rC <= rA >> rB
  srai rC,rA,IMMED5 rC <= rA >> IMMED5
  Logical shifts fills vacated bits with 0’s
  Arithmetic shifts extend the sign bit on the left
Rotates
  ror rC,rA,rB
  rol rC,rA,rB
  roli rC,rA,IMMED5
  Rotate differs from a shift in that the bits shifted out of one end are wrapped around to the other end

## Slide 16: Common Instructions (con’t)
Unconditional Branch
  br LABEL
  I-type instruction. Immediate operand (16bits) is the offset from current program location to LABEL
Conditional Branch
  blt rA,rB,LABEL //branches if rA < rB
  beq rA,rB,LABEL //branches if rA = rB
  Also unsigned comparison

## Slide 17: Memory Access
Read: ldw r3, 4(r5) //copies value from memory to r3
Write: stw r3, 4(r5) //copies r3 value to memory
Ex: If r5 contains the value 0x100, then the memory location accessed for both the ldw and stw would be 0x104.
destination
source
Effective address: adds constant 4 to
contents of r5 to form the address

## Slide 18: Load and Store
No ldi or sti (immediate load or store)
  How do you put 0x100 into r5?
  addi r5, r0, 0x100
For memory access
  ldw, stw : load and store word
  ldb, stb : load and store byte
  ldh, sth : load and store half word
For memory mapped io
  ldwio, stwio, ldbio, stbio, ….
  Bypasses the cache

## Slide 19: Memory Structure
Memory is organized in words
  32 bits or 4 bytes
  Each word has an address
                Why do the addresses jump by 4?
Address | Data
0x0000 | 32 bit value
0x0004 | 32 bit value
0x0008 | 32 bit value
0x000C | :
: | :
: | :
0xFFFC | :

## Slide 20: Memory Structure (con’t)
Because data is byte addressable memory effectively looks like this:
Address | Data
0x0000 | 8 bit value
0x0001 | 8 bit value
0x0002 | 8 bit value
0x0003 | 8 bit value
0x0004 | :
: | :
0xFFFC | :

## Slide 21: Memory Structure (con’t)
Consider the following data:
It is stored like this:
Address | Data
0x0000 | 0x12345678
0x0004 | 0xABCDEF00
Address | Data
0x0000 | 0x78
0x0001 | 0x56
0x0002 | 0x34
0x0003 | 0x12
0x0004 | 0x00
0x0005 | 0xEF
LSB has smallest address:
called little endian
What value is put into r3 with the following
instruction, assuming r5 contains 0x0001?
ldw r3, 2(r5)

## Slide 22: Example code

## Slide 23: Subroutines
Similar to a function call in C
Execution leaves the main program and jumps to a code segment that performs a specific function
Especially useful if there is a function that needs to be done several times in a program
Must end with ret

## Slide 24: Subroutine Example