## Slide 1: NIOS II Processor

## Slide 2: Reminders
Quiz due on Sunday
  Assembly, NIOSII, and Embedded SW lectures
No demo this week on Friday – Class Cancelled
Lab 1 due
Lab 2 prelab due

## Slide 3: Last Weeks Questions
What is a caller saved register?
  Volatile registers used to hold temporary values that need do not need to be preserved between calls
  Call refers to a procedural access
  Callee saved registers are non-volatile and must be saved if a function needs to overwrite the value
Can a stw offset be a register? No

## Slide 4: Processor Types - CISC
CISC Processor Architecture
  CISC  Complex Instruction Set Computer
    Processors that are easy to program and make efficient use of memory.
    Earliest machines were programmed in assembly language and memory was slow and expensive
      Big programs require a lot of memory $$$$
  CISC developed to make compiler development simpler
    Shifts burden of generating machine instructions to the processor
    Ex: Instead of compiler writing long machine instructions to calculate a square-root ability was built-in CISC processor
    Instructions require multiple clock cycles to execute
  Examples:
    Intel 80x86
    Motorola 68K series

## Slide 5: CISC Processors
CISC Instruction Sets
  More complex instructions
    Instruction fit into multiple words
    More complex hardware
    Shorter programs
  Complex address modes supported
  Memory-to-memory transfer supported

## Slide 6: Processor Types - RISC
RISC Processor Architecture
  RISC Reduced Instruction Set Computer
    Processor architecture that uses small, highly-optimized set of instructions
  RISC Characteristics
    one cycle execution time
      RISC processors have a CPI (clock per instruction executed)
    Pipelining
      Technique for simultaneous execution of instructions
    Large number of registers
      Prevent large interactions with memory
  Examples:
    ARM
    Nios II
    PowerPC

## Slide 7: RISC Processors
RISC Instruction Sets
  Simpler instructions
    Instruction fits into single word
    Simpler hardware
    Faster instruction execution
    Longer programs
  Simpler address modes
  Load/Store architecture used
    Memory only access via load/store instructions
    Arithmetic/logic operations work on register

## Slide 8: Processor Types
CISC | RISC
Emphasis on hardware Software simple | Emphasis on software Hardware simple
Includes multi-clock, complex instructions | Single-clock, reduced instruction only
Memory-to-memory: "LOAD" and "STORE" incorporated in instructions | Register to register: "LOAD" and "STORE" are independent instructions
Small code sizes, high cycles per second | Low cycles per second, large code sizes
Transistors used for storing complex instructions | Spends more transistors on memory registers
RISC systems shorten execution time by reducing the clock cycles per instruction (i.e. simple instructions take less time to interpret)
CISC systems shorten execution time by reducing the number of instructions per program

## Slide 9: Processor Types
CISC and RISC Processor Architecture
  Line between RISC and CISC blurring
    CISC processor borrowing goodness from RISC
      Ex: Pipeline introduced into CISC
    RISC processor borrowing goodness from CISC
      Ex: More complex addressing added into RISC

## Slide 10: Nios II Processor Overview
What is the Nios II Processor?
  Soft-core processor developed by Altera (now Intel)
    Soft core design  not fixed in silicon
    Soft core allows customizing of processor and peripherals
      Add processor features as required
      Remove unused processor features
      Create custom instructions
  Nios II is second generation of software processor
  32-bit RISC Processor
    RISC Simple instructions provide higher performance
      If instructions are simple enough to execute very quickly

## Slide 11: NIOS II Basics
General-purpose RISC processor core
  32-bit instruction set, data path and address space
  32 general-purpose registers
  Optional shadow register sets – useful for context switching and multitasking systems (RTOS)
  32 interrupt sources
  External interrupt controller interface for more interrupt sources
  Single instruction 32 x 32 multiply and divide producing a 32 bit result
  Dedicated instructions for computing 64-bit and 128-bit products of multiplication
  Floating-point instructions for single-precision floating-point operations

## Slide 12: NIOS II Basics (con’t)
  Single-instruction barrel shifter
  Access to a variety of on-chip peripherals, and interfaces to off-chip memories and peripherals
  Optional memory management unit (MMU) to support operating systems that require MMU
  Optional memory protection unit (MPU)
  Instruction set architecture (ISA) compatible across all NIOS II processor systems

## Slide 13: NIOS II Processor System
A NIOS II processor system is equivalent to a microcontroller that includes a processor, memory and a combination of peripherals
Example system
Processor
Off-chip
memory
On-chip
memory
Input/
Output
Peripherals

## Slide 14: NIOS II Architecture
The NIOS II architecture defines the following functional units:
  Register file
  Arithmetic logic unit (ALU)
  Interface to custom instruction logic
  Exception controller
  Internal or external interrupt controller
  Instruction bus
  Data bus
  Memory management unit (MMU)
  Memory protection unit (MPU)
  Instruction and data cache memories
  Tightly-coupled memory interfaces for instruction and data
  JTAG debug module

## Slide 15: NIOS II Architecture

## Slide 16: NIOS II Architecture
The functional units of the NIOS II architecture form the foundation for the NIOS II instruction set
  This does not indicate that any unit is implemented in hardware
  The NIOS II architecture describes an instruction set, not a particular hardware implementation
  A functional unit can be implemented in hardware, emulated in software or omitted entirely
A NIOS II implementation is a set of design choices embodied by a particular NIOS II processor core
  Each implementation achieves specific objectives such as smaller core size or higher performance
  Allows the NIOS II architecture to adapt to the needs of different target applications.

## Slide 17: NIOS II Processor Tradeoffs
Implementation variables generally fit one of three trade-off patterns:
  More or less features
    Example: To fine-tune performance, you can increase or decrease the amount of instruction cache memory. A larger cache increases execution speed of large programs, while a smaller cache conserves on-chip memory resources
  Inclusion or exclusion of a feature
    Example: To reduce cost, you can choose to omit the JTAG debug module. This decision conserves on-chip logic and memory resources, but it eliminates the ability to use a software debugger to debug applications.
  Hardware implementation or software emulation of a feature
    Example: For applications that rarely perform complex arithmetic, you can choose for the division instruction to be emulated in software. Removing the divide hardware conserves on-chip resources but increases the execution time of division operations

## Slide 18: Memory and I/O Organization
The flexible nature of the NIOS II memory and I/O organization are the most notable difference between NIOS II processor systems and traditional microcontrollers
Because NIOS II processor systems are configurable, the memories and peripherals vary from system to system
  As a result, the memory and I/O organizations varies from system to system

## Slide 19: Memory and I/O Organization
A NIOS II core uses one or more of the following to provide memory and I/O access:
  Instruction master port – An Avalon Memory-Mapped (Avalon-MM) master port that connects to instruction memory via system interconnect fabric
  Instruction cache – Fast cache memory internal to the NIOS II core
  Data master port – An Avalon-MM master port that connects to data memory and peripherals via system interconnect fabric
  Data cache – Fast cache memory internal to the NIOS II core
  Tightly coupled instruction or data memory port – interface to fast on-chip memory outside the NIOS II core
The NIOS II architecture hides the hardware details from the programmer so programmers can usually develop applications without specific knowledge of the hardware implementation

## Slide 20: Memory and I/O Organization

## Slide 21: Memory and I/O Organization
The NIOS II architecture does not specify anything about the existence of memory and peripherals; the quantity, type, and connection of memory and peripherals are system-dependent
  Typically, NIOS II processor systems contain a mix of fast on-chip memory and slower off-chip memory
  Peripherals typically reside on-chip, although interfaces to off-chip peripherals also exist

## Slide 22: Two Types of Processor Architectures
Harvard
  Has physically separate signals and storage for code and data memory
  Two data buses and two address buses
  Instructions can be fetched simultaneously with data being fetched
VonNeumann
  Shared signals and memory for code and data
  One data bus and one address bus
  Program can be modified by itself

## Slide 23: Two Types of Processor Architectures

## Slide 24: Instruction and Data Buses
The NIOS II architecture supports separate instruction and data buses, classifying it as a Harvard Architecture
  Both the instruction and data buses are implemented as Avalon-MM master ports that adhere to the Avalon-MM interface specification
  The data master port connects to both memory and peripheral components, while the instruction master port connects only to memory components
    Known as memory-mapped I/O – both the memory and peripherals are mapped into the address space of the data master port
    Use pointers to addresses in programs to access both memory and I/O

## Slide 25: Two Types of Data Storage
Endian describes the order in which bytes of data are stored in memory

## Slide 26: Data Storage
The NIOS II architecture is little endian
  Words and halfwords are stored in memory with the more-significant bytes at higher addresses
Words in NIOS II are 32 bits
  In ESD 1, when in doubt, the answer is 32!
31 |  |  | 0
N + 3 | N + 2 | N + 1 | N

## Slide 27: Nios II Processor Overview (Classic)
Three levels of Performance
  Allows design scale as requirements change

## Slide 28: Nios II Processor Overview (Classic)
Three level of Performance
  Performance & Size
    Performance varies by factor of 9
    Size varies by factor of 3

## Slide 29: NIOS II Processor Overview
Our version of Platform Designer suggests not using classic
We will choose between NIOS II/e and NIOS II/f
We will be using NIOSII/e this semester, but the default is NIOSII/f
Be sure to choose the correct processor!