## Slide 1: Embedded Software Design

## Slide 2: Reminders
Quiz due Sunday by midnight
  Assembly, NIOSII, and Embedded SW
No demo this week on Friday – Class Cancelled

## Slide 3: Follow Up
Can we use the name of the register when executing instructions?
  Yes! Replace r0 reference with the word zero
  Step through assembly, works with no issues

## Slide 4: Follow Up
How do we work with IMMED values larger than 16 bits?
  Approach 1 –
    Register instructions allow you to work with numbers larger than 16 bits
    Create a variable with 32 bit number
    Add that constant and r0 and store in another register
    Now you may use 32 bit number for functions
  Approach 2:
    Use NIOSII macro instructions
    Could also be done manually
      Easy with binary and hex numbers

## Slide 5: Two Types of SW Development
Desktop Software Development
  Written and debugged on the same machine as target
  OS loads programs when program runs
  Address resolution occurs when program is loaded
    Loader is part of OS
  Memory is usually not major concern
Embedded Software Development
  Written and debugged on different machine as target
    Cross-compiler run on host (development machine)
  Downloaded to target for hardware/software integration

## Slide 6: Embedded Software Development
Build creates an Executable & Linkable Format File (ELF)
    Contains: Boot code, Application, RTOS (optional)
    Downloaded to board to run on processor
Designer manages address map of peripherals
Designer manages location of application in memory
Amount of memory depends on
    Amount required for instructions
    Amount required for data
    Amount you can afford in terms of $$$, power & board space

## Slide 7: Embedded Software Development
Embedded SW Design Challenges
  Software designed for specific function & target
  Software tightly coupled with hardware design
    Hard to debug if hardware is not available
    Hard to debug real-time I/O
  Real-time response
    Requires deterministic response
    May require code optimization
    RTOS
  Reliability
    Failures are typically not tolerated
  Ex. Launching Word vs. Pushing a brake pedal

## Slide 8: Embedded Application Stack

## Slide 9: Application Stack w/RTOS

## Slide 10: Device Drivers
Software developed to interact with hardware
  Written for specific hardware and operating system
  OS or application software interacts transparently with HW
Provide a level of abstraction by hiding details of HW
  Converts application function calls into device specific calls
  Allows hardware to change w/o effecting OS or application
    Ex: swap out PC video card  load new drivers
Writing device drivers requires specific hardware knowledge
  Bugs tend to be serious because drivers run at privileged level
Application Program Interface API
  Defines function call OS or application uses for lower level drivers

## Slide 11: Hardware Abstraction Layer (HAL)
The HAL provides a simple device driver interface for programs to connect to the underlying hardware
The HAL application program interface (API) is integrated with the ANSI C standard library
The HAL API allows access to devices and files using familiar C library functions
  Printf(), fopen(), fwrite(), etc.
The HAL serves as a device driver package for NIOS II processor systems
  Provides a consistent programming interface to the peripherals in a NIOS II system
Nios II

## Slide 12: HAL Architecture and Services
Integration with the newlib ANSI C standard library
  Provides the familiar C standard library functions
Device drivers
  Provides access to each device in the system
The HAL API
  Provides a consistent, standard interface to HAL services, such as on-chip peripheral access, interrupt handling and alarm facilities
System initialization
  Performs initialization tasks for the processor and the runtime environment before main()
Device initialization
  Initializes each device in the system before main() runs
Nios II

## Slide 13: Layers of NIOS II HAL-Based System

## Slide 14: Levels of Languages
Programming languages
  Machine Code
    Basic language of computers  ones and zeros
    Machine dependant
    Hard to read, program and maintain
  Assembly Language
    Uses mnemonics to improve readability
      Representation of machine language
    Used for code where size or speed is critical
    Used to access special commands or hardware
    Disadvantages
      Longer programs than high level languages
      Machine dependent code

## Slide 15: Levels of Languages
Programming languages
  High level Languages
    Hardware independent
    More human readable
    Ex: C, Pascal, etc
  Very High Level Languages
    Hardware independent
    More human readable
    Object-oriented languages
      Ex: C++, Java

## Slide 16: Language Level Summary
 | Language | Description
1st Generation | Machine Code | Binary (0,1) and hardware dependent
2nd Generation | Assembly language | Hardware dependent but at a more readable format using mnemonics
3rd Generation | High-Level Languages | Higher level language more like English words that makes code more readable. Code is also more portable between platforms because it is not machine dependent.
4th Generation | Very High Level Languages | The next still in evolution of high level languages where code is objects are used.
5th Generation | Natural Languages | Languages that are very similar normal conversation. Used in artificial intelligent. Still in development.

## Slide 17: Tools and Resultant Files
Compiler
  Tool that translates high-level languages into Assembly
Assembler
  Tool that translates ASM into machine language
  Reads ASM to produce object files
Object files
  Contains machine instructions & other book keeping info
  Can be executed if it does NOT contain unresolved references to other object files or libraries
  Every object file has sections
    Sections organize code by common characteristics
    Sections may or may not have any contents
      Empty sections have memory reserved

## Slide 18: Tools and Resultant Files
Linker
  Tool that combines object files into single executable
  Searches program libraries to find library routines
  Determines the memory locations that code will occupy and adjust absolute references
  Resolve all references (labels) among object files
  Linking is controlled by linker script file
    Defines how input files are mapped to output files
    Controls where code sections are mapped to memory

## Slide 19: Linker Tool
Linking libraries
  Static linking
    Libraries routines are linked into executable
      Executables become large
      Executable can’t access libraries updates w/o being recompiled
  Dynamic Linking (DLL)
    Library linked and loaded at run-time
    Avoids linking entire library into executable
    Executable can link in new library updates at run-time
    Requires extra space for DLL but smaller than entire library
    Small run-time penalty to load library dynamically

## Slide 20: Software Design Flow Example
Executable and Linking Format File (*.elf)
  Created when you build Nios II program
  Runs on Nios II processor

## Slide 21: Object File
Typical Object Sections
  .text
    Only executable code goes here
  .rodata and .sdata2
    Contains read-only data
    Ex: Print strings and constants
  .data and .sdata
    Contains read/write data
  .bss and .sbss
    Uninitialized data (variables)

## Slide 22: Object Files
Dumping Object Files
  Object dump will show memory address of various sections
  Critical information for debugging embedded software
  Must launch Nios II command shell
    Launch from Program  Intel_FPGA  NiosII
  Change directory to location of executable file
    To dump help
      nios2-elf-objdump
    Dump header locations
      nios2-elf-objdump -h
    Dump code source
      nios2-elf-objdump –S
Nios II

## Slide 23: Object Files
nios2-elf-objdump
  Sample help screen
Nios II

## Slide 24
Dumping Object Files
Nios II
Size of section in bytes
Virtual Memory Address
Load Memory Address

## Slide 25: Object File
Dumping Object Files
  The LMA and VMA may differ
    ROM based system
      Loading a data section into ROM and then copying it into RAM
      LMA would be associated with the ROM
      VMA associated with the RAM
Nios II

## Slide 26: Object File
Dumping Object Files
  Nios II SBTs generate *.objdump file
    Text file located in your Nios II application directory
    Provides information about your .elf such as
      Information about the memory sections and their layout,
      Addresses of functions, w/ C code interleaved w/ assembly
    To enable right-click your application project and click Properties
      Click Nios II
        Application Properties
      On Properties page
        turn on Create object dump.
Nios II

## Slide 27: Map File
Nios II SBT generate *.map file
  Text file located in your Nios II application directory
  Provides information including which object files are included in the executable, the path to each object file, where objects and symbols are located in memory, and how the common symbols are allocated
  Good for finding variables in memory and peeking them for debug
Nios II

## Slide 28: Embedded Software Considerations
Compiler Optimizations
  Procedure Inlining
    Replacing functions call with actual code to avoid overhead of call
  Loop Unrolling
    Replicating loop body & reducing the loop counter
      Must understand loop behavior
    Reduces loop overhead (test and jump)
    Example:
      for i = 1 to 10
      <do some work>
      after loop unrolling may become
      for i = 1 to 5
      <do some work>
      <do some work>

## Slide 29: Embedded Software Considerations
Compiler Optimizations
  Common sub-expression elimination
    Finding multiple instances of same expression and replace 2nd reference with reference to first
    Example:
      A = B * C + G
      E = B * C + M
      after sub-expression elimination become
      X = B * C
      A = X + G
      E = X + M
  Strength reduction
    Replacing complex operations with simpler operations
    Machine dependent
    Ex: Replacing multiply with a shift

## Slide 30: Embedded Software Considerations
Compiler Optimizations
  Dead Store Eliminations
    Removing stored values that are not used
    Eliminates overhead of doing store
  Dead Code Eliminations
    Removing Code that does not effect final result
  Code Motion
    Removing code from loops that doesn’t effect the loop
    Ex:
      Loop on I
        A=B+C // can be moved above loop
        D=A+X[i]
      End loop

## Slide 31: Embedded Software Considerations
Compiler Optimizations
  Constant propagation
    Replace all instances of a variable that is assigned a constant with constant
    Ex:
      X = 3; x = 3;
      Y = X + 4 Y = 7;
  Copy propagation
    Copy variable value to avoid re-loading value
    Ex:
      Y = X;
      Z = Y + 4 Z = X + 4;
  Pipeline Scheduling
    Reordering instructions to improve pipeline scheduling
 Becomes 
 Becomes 

## Slide 32: Embedded Software Considerations
When do you not want optimized code?
  When debugging code
    Not concern with speed of program
    Want to be able to trace logical flow of program
      Similar to functional simulation in VHDL
  Conflicts with embedded design feature
    Real-time response may require optimization for performance
Problems with optimized code
  Code may work with no optimization but fails with compiler optimization is enabled
  Most common problem is missing volatile type qualifier

## Slide 33: Embedded Software Considerations
Compiler Optimizations
gcc Optimization Levels:
Off (-O0)
  -Fast compile
On and Level 1 (-O -O1)
  -Speed and size optimization
Level 2 (-O2)
  -Full optimization without speed-space tradeoff
Level 3 (-O3)
  -Full optimization, larger size
Size (-Os)
  - Optimize space usage
Notes: Level 3: O3 uses agrees inlining of subprograms and makes the program much larger

## Slide 34: Embedded Software Considerations
Options for Code Footprint Reduction
  Enable Compiler size optimizations
    -Os or -03
  Use reduce device driver
  Use ANSI C library
  Remove clean exit
    If code runs forever then you don’t need clean exit
  Disable C++ support
  Enable lightweight device driver API
    Only stdin, stdout and stderrr file descriptor supported
    -Os or –O3

## Slide 35: Embedded Software Considerations
Good Practices
  Use volatile for registers and user input accesses
  Allocate memory in advance
    Good to bound memory required for application
      Define fixed arrays to hold data
      Avoid using malloc to allocate memory
  Control pointers offsets
    Check if offsets are in bounds
    Arrays help perform checks
  Place constants on left when performing check
    Ex:
      if (MAX_VALUE == variable)
      Instead of
      if (variable == MAX_VALUE)